## Slide 1: Riistvara ja operatsioonisüsteemide alused HKI5085.HK
Martti Raavel
MRT@TLU.ee

## Slide 2: Mis jäi eelmisest korrast segaseks?
Miks näevad graafikakaardid nii erinevad välja (mõnel on propeller/jahuti?) ja teistel on hallid pulgad. Graafikakaardi tööpõhimõttest tahaks ka paremini aru saada.
Kus mingid juhtmed täpselt emaplaadi peal käivad ja et miks osad juhtmed jäid lahtiseks

## Slide 3: Tänane tund
Test eelmiste kordade materjali kohta
Kodutööde esitlused
Lisaseadmed
Operatsioonisüsteemid …

## Slide 4: LISASEADMED
Monitor (ekraan)
Printer
Skanner
Kaamera
…
https://encrypted-tbn0.gstatic.com/images?q=tbn:ANd9GcRWxT9vg4ZyO6Oa4FF6k1SUdLFoqunm0DvRySKrqWpJLvjnhuQN
https://i.stack.imgur.com/yVETd.jpg
http://www.freeimageslive.com/galleries/transtech/informationtechnology/pics/handy_scanner.jpg

## Slide 5: Monitor
Suurus (tollides)
Resolutsioon ja punktitihedus (HD, Full HD, 4K)
Külgede suhe (4:3, 16:9, 21:9, …)
Värvide hulk, heledus, kontrastsus
Läikiv / matt
Värskendussagedus (refresh rate)
CRT, LCD, Plasma, LED
https://www.maxpixel.net/static/photo/2x/Commodore-Crt-Screen-Computer-Device-Electronic-1299461.png
Notes: CRT - cathode-ray tube
DPI / PPI 70-90, mobiiltelefonidel 300 – 500!
Full HD – 1920x1080, 2560 x 1440, 3840 x 2160, 7680 x 4320
Aspect ratio
Plasma – pikslid täidetud gaasiga, pikslid kaetud ainega mis hakkab helendama
LCD – vedelkristallid, blokeerivad, lasevad valgust läbi, ise ei helenda, vajalik taustavalgustus

## Slide 6: CRT, LCD, LED, OLED, QLED, …
https://upload.wikimedia.org/wikipedia/commons/1/17/Medion_CRT-Monitor_19%22_Silber-Metallic.jpg
https://pixy.org/src/516/5164250.jpg

## Slide 7: LCD/LED
http://desktopreality.com/wp-content/uploads/2012/03/ccfl.jpg
http://desktopreality.com/wp-content/uploads/2012/03/ledbacklit.jpg

## Slide 8: Vaatame ise järele
Vaatame, mis on ühe LCD või LED ekraani sees

## Slide 9: PRINTER
Must / värviline
Liides (Paralleelport, USB, LAN, Wifi)
Kiirus (ppm, lk/min)
Formaat
Prinditihedus (lahutusvõime, dpi)
Müratase
Kahepoolne printimine (duplex)
???
https://upload.wikimedia.org/wikipedia/commons/a/a3/Star-LC-10-printer-01.jpg
Notes: printimine on info automaatväljastus arvutist paberile (http://eki.ee/dict/qs/index.cgi?Q=printimine)

## Slide 10: Printer
Maatriksprinter
Tindiprinter
Laserprinter
Õisprinter???
Termoprinter
Sublimatsioonprinter
Vahaprinter
3D printer
…
https://cdn.pixabay.com/photo/2014/05/14/10/35/printers-344016_960_720.jpg
Notes: Sublimation is a chemical process where a solid turns into a gas without going through a liquid stage.

## Slide 11: Maatriksprinter
https://www.google.com/url?sa=i&source=images&cd=&ved=2ahUKEwjM2ZK0z5TlAhUStosKHdeHCUMQjRx6BAgBEAQ&url=https%3A%2F%2Fcommons.wikimedia.org%2Fwiki%2FFile%3APrinter_dot_matrix_EPSON_VP-500.jpg&psig=AOvVaw058Oj2Dg6CrWWS_-GJSg_R&ust=1570897481077034
https://cdn.comboink.com/blog/wp-content/uploads/2018/05/dot-matrix-example-text.png
Väga odav kasutada
Suur müratase
Aeglane
Hind alates u 200.-

## Slide 12
https://www.google.com/url?sa=i&source=images&cd=&ved=2ahUKEwjen7GK0JTlAhWro4sKHc-sC2cQjRx6BAgBEAQ&url=http%3A%2F%2Fitblogs.in%2Fcomputers%2Fhardware%2Fprinters%2F&psig=AOvVaw2SfiLeaBjCxmLdENZQe3Mg&ust=1570897425466050

## Slide 13: Tindiprinter
Odav väljatrükk?
Hea trükikvaliteet
Väike
Kiire esimese lehe väljatrükk
Kuivab ära 
https://www.graphicproducts.com/media/71445/inkjet.jpg
Notes: Epson Ecotank
Printeri tint / pea koos eraldi

## Slide 14: EPSON ECOTANK
https://mediaserver.goepson.com/ImConvServlet/imconv/7e6faf7f18a7d9382d29554821b86e35eab84771/original?use=productpictures&assetDescr=fg_printer-with-inks

## Slide 15: Laserprinter
Odav?
Kiire
Täpne
Voolutarve
Fotokvaliteet?
Varjatud kulud?
https://www.staples.co.uk/content/images/product/GenesisExtraLarge/71/49/asset.5387149.jpg
Notes: Ka LED printer

## Slide 16: Laserprinter
http://www.dginter.net/cst/2011CST/Chapter07/old/UnitBPrinters/old/dev/HowStuffWorks/How%20Laser%20Printers%20Work_files/laser-printer-laser.gif

## Slide 17: 3D printer
https://static.bhphoto.com/images/images2500x2500/1504625769_1359320.jpg
Stereolithography (SLA)
Fused Deposition Modeling (FDM)
Selective Laser Melting (SLM)
Laminated Object Manufacturing (LOM)
Notes: SLA vedelikust laseriga
FDM ”tavaline”
SpaceX!!!

## Slide 18: Skänner
Optiline sisendseade, mis loeb paberilt teksti ja pilte ning teisendab kujutise ridahaaval digitaalsele kujule, nii et seda saab arvutiga töödelda, kuvada ja printida.
http://vallaste.ee/
https://static.bhphoto.com/images/images2000x2000/1481196164_1114127.jpg

## Slide 19: Skänner
Kiirus (ppm)
Punktitihedus (dpi)
Värvisügavus (bit)
Liides
Suurus
http://www.extremetech.com/media/images/13636.gif?thumb=y
Notes: CCD (charge-coupled device)

## Slide 20: Multifunktsionaalne printer
Printer + skänner
Parem või halvem?
https://www.shoppa.ee/i/pyrg/products/480x480/2/2/8/6/2286591_epson-multifunctional-printer-l6190-colour-inkjet-cartridge-free-printing-a4-wi-fi-black.jpg

## Slide 21: Kodune töö
Väljapääsupilet
Esitluste teemad:
  Windows
  MacOS
  Ubuntu
  Android
  Unix

## Slide 22: Allikad:
https://www.viewsonic.com/library/business/monitor-resolution-aspect-ratio
https://www.lifewire.com/lcd-vs-plasma-tv-1847462
https://www.printi.com/blog/sublimation-printing/
https://kb.iu.edu/d/adme
https://desktopreality.com/led-monitors-the-myth-and-the-fact/
https://www.printernet.co.uk/blog/advantages-of-inkjet-printers-2175/
http://www.dginter.net/cst/2011CST/Chapter07/old/UnitBPrinters/old/dev/HowStuffWorks/How%20Laser%20Printers%20Work.htm
https://whatis.techtarget.com/definition/volt-ampere-VA
https://study.risk.ee/arvuti/kkk/kuidas-lcd-pilti-naitab/
https://www.webopedia.com/TERM/O/operating_system.html
http://www.tlu.ee/~nullyks/opsys_slaidid.pdf
http://www.teach-ict.com/2016/GCSE_Computing/AQA_8520/3_4_computer_systems/344_systems_architecture/memory/miniweb/pg7.htm